## Slide 1: Brief Intro to Geospatial Data
Modified from “Overview of Geospatial Data” by Patty Frontiera, Drew Hart, and Hikari Murayama of UC Berkeley’s D-Lab, used under CC BY-NC-SA 4.0.
Notes: To get us started, and before we dive into any coding, let’s go over some core geospatial concepts.
Q: Raise your hand if you’ve worked with geospatial data before
More figures for later: https://www.geoawesomeness.com/top-7-maps-ultimately-explain-map-projections/

## Slide 2: Geospatial data
Anatone, WA: 46.130479, -117.134167
BUT, how do we know that those coordinates reference that specific location?
Notes: So Geospatial Data is a location that is given by a set of coordinates. Anatone WA has specific coordinates associated with its location, a latitude and a longitude. The specific values we use to answer the question of “where” can differ by the coordinate reference system we use.

## Slide 3: Coordinate Reference Systems (CRS)
A Coordinate Reference System, or CRS, is a system for associating coordinates with a specific, unambiguous location on the surface of the Earth.
New Orleans = 30N, 90W
Notes: Coordinate References Systems, or CRS for short, is a way to give numerical coordinates for a position on earth. So for Anatone, WA we used a specific pair of latitude and longitude numbers to specify where it is on planet earth.

## Slide 4: Coordinate Reference Systems (CRS)
http://latitude-longitude.net
Geographic Coordinates: Latitude and Longitude
Notes: These latitude and longitude pairs are what make make geometries geographies! With this pair of numbers you can point to a specific point on the globe.

## Slide 5: Coordinate Reference Systems (CRS)
There are many CRSs, not just one!
Why? Because our understanding of and ability to measure the shape of the earth has changed over time.
Notes: Anatone, WA could actually have different pairs of values depending on the CRS we use. This is because there are different CRSs, with each one based on a different set of knowledge about the shape of our earth. Well what do I mean by that...

## Slide 6: Two Types of Coordinate Reference Systems
Geographic CRS
Projected CRS
Angular Units = Degrees (DMS or DD)
Cartesian Units = Feet or Meters
Good for local & regional mapping & analysis
Notes: So we have two types of CRS: Geographic and Projected
GCS is good for storing data and has units of degrees
PCS is good for analyzing data and has units of feet or meters
Let’s go through these two types in detail

## Slide 7: Geographic Coordinate Systems (GCS)
Widely used! Expressed as latitude & longitude
WGS84 (EPSG: 4326)
Based on satellites, used by cell phones, GPS
Best overall fit for most places on earth
NAD83 (EPSG: 4269)
Based on satellites and survey data
Best fit for USA
Used by many federal data products, like Census data
CRSs are referenced in software by numeric codes, often called EPSG codes
Notes: GCS are actually quite popular and as you become more familiar with geospatial data and work with different datasets, two CRS you will probably run into are WGS84 and NAD83.
Why do you think people will use different CRS for different places or reasons? Sometimes different CRS work better in one location rather than another. NAD83 is actually great to use if you’re looking at the US. Those 4 digit numbers you see next to NAD83 is the EPSG code. These codes are what you’ll be using in Python and R to designate a specific CRS.

## Slide 8: Earth is not flat!
But computer screens, paper maps and most of the math underlying spatial analysis methods assume it is!
We use map projections to transform geospatial data from a 3D model of the earth to a 2D plane.
This causes distortion :(
You need to understand how this might impact your maps and spatial analysis!

## Slide 9
Notes: Image source: https://www.esri.com/arcgis-blog/products/arcgis-pro/education/earth-peel/
Here is our orange… let’s pretend now that it is perfectly spherical

## Slide 10
Notes: Image source: https://www.esri.com/arcgis-blog/products/arcgis-pro/education/earth-peel/
Ta-da! And we’ll go ahead and draw all of our continents on here. Now that we have this lovely rendition of earth, we’ll go ahead and peel it.

## Slide 11
Notes: Image source: https://www.esri.com/arcgis-blog/products/arcgis-pro/education/earth-peel/
And here’s one way to peel it,. This looks pretty similar to the maps you see when you google “world map” or the ones that were hung up in your elementary school classroom. But then thing is you can peel an orange multiple other ways

## Slide 13: Projected Coordinate Systems (PCS)
Map Projections transform geographic coordinates (lat/lon) to 2D coordinates (X/Y)
All map projections introduce distortion in area, shape, distance or direction.
Specific map projections minimize distortion in one or more properties
You need to know the coordinate reference system of your input data
You need to select the CRS that is most suitable for your data and application.
Notes: PCS on the other hand introduce distortion since we’re looking at our locations on a flat plane. But this makes them great for area, shape.. And general measurements of distance. As with GCS, PCS also have some systems that are better for some locations other than others.

## Slide 14: Types of Spatial Data
There are two fundamental types of spatial data:
Vector
Raster
Notes: Geospatial data can be divided into two categories--- vector and raster.

## Slide 15: Vector Data
“Connect the dots”
Notes: Vector data can be thought of data that you can connect the dots with. This type of data can include points, lines, and polygons.

## Slide 16: Points, Lines, Polygons
Notes: Each of these geometry types can be for a different type of information. Points could be great for showing us where crimes have occurred historically. Lines could show us the location and length about where freeways are in the city. Polygons could help us show different information about different neighborhoods.

## Slide 17: Vector Data with Attributes
Each row represents one geospatial feature
Attributes describe the features (fields or columns)
Each feature has an associated geometry or geometry collection
A group of features is called a layer
Notes: We’ll now briefly talk about what this vector data looks like when you open it up.
You might get something like the table you see on the right side of the screen. Each row represents one geospatial feature. So for our second attribute we have the ID number 2, the plot size 20, vegetation type, and a vegetation class of deciduous. Those additional information I just rattled off to you like the plot size, are attributes. These help describe our features.
Furthermore, each of these features have an associated geometry or geometry collection. So in our first table our geometry is a point,
One last thing about vector data-- each group of features is called a layer. So you could have all three of these data, and each dataset would be its own layer.
I’ll pause for a moment for any questions. Feel free to drop them in the chat or unmute to ask your question.

## Slide 18: Raster Data - regular grids
A location is represented by a grid cell
Cells have regular size, eg 30x30m
Grid has dimension - fixed number of rows and columns
Each cell has a value that represents the attribute of interest, e.g. elevation
(Digital Elevation Model)
Notes: Now let’s go to Raster data! Do you notice anything about this image that seems different from what we had looked at for vector data?
RIght, so raster data looks more continuous. Our dataren’t defined by geometries--- rather, it’s like this quilt of little squares, each square holding a value. These squares could be something like 30 by 30meters, and each one could hold information such as elevation.

## Slide 19: Categorical Raster Data
30m pixels

## Slide 20: Images are Raster Data
Source: BING Aerial imagery
Notes: One common raster data type is images! If you zoom way way in into this something like this picture, you’d see squares of different colors.

## Slide 22: Vector vs Raster
Vector data are better for
discretely bounded data
e.g. political boundaries, fire hydrants, rivers, roads, etc.
Raster data are better for
continuous data
e.g. temperature, elevation, rainfall, etc.
Image: http://gsp.humboldt.edu/
Notes: Now that we know we have these two types of datasets, we can talk about when to use each. Vector data are better for when you have discreetly bounded data. This could be for counties, rivers, etc. On the other hand, raster data is better for continuous data (like the image we just looked at), or maybe something like temperature, elevation or rainfall.

## Slide 23: Some Common File Formats
Vector Data
Shapefile (.shp…)
GeoJSON, JSON
KML
GeoPackage
Raster Data
GeoTIFF
netCDF
DEM
Notes: Now these two datasets come in different file formats, so you’ll know what it is before you pull it in for whatever GIS software you’re using. Some common ones I use are shapefile and geojsons for vector data, and geotiffs for raster data.

## Slide 24: Georeferencing
Data layers in the same coordinate reference system can be linked to explore associations
Notes: Although these two types of data look different, and come in different formats, you can still use a combination of raster and vector data to answers questions that you’re probably aiming to answer through your own work.
I’m going to take a second breather here before we move on. What kind of questions do you all have?